## Slide 1
Register Transfer and Micro-operations 1 Lecture 6
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT
Overview
Register Transfer Language
Register Transfer
Bus and Memory Transfers
Arithmetic Micro-operations
Logic Micro-operations
Shift Micro-operations
Arithmetic Logic Shift Unit

## Slide 2
Register Transfer and Micro-operations 2 Lecture 6
Register Transfer Language
Combinational and sequential circuits (learned in Lecture 1 and 2) can be used to create simple digital systems.
These are the low-level building blocks of a digital computer.
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.
The operations on the data in registers are called micro-operations
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 3
Register Transfer and Micro-operations 3 Lecture 6
Register Transfer Language
Set of registers and their functions
Micro-operations set
Set of allowable micro-operations provided by the organization of the computer
Control signals that initiate the sequence of micro-operations (to perform the functions)
Definition of the (internal) organization of a computer
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 4
Register Transfer and Micro-operations 4 Lecture 6
Register Transfer Language
Rather than specifying a digital system in words, a specific notation is used, Register Transfer Language
For any function of the computer, the register transfer language can be used to describe the (sequence of) micro-operations
Register transfer language
    A symbolic language
    A convenient tool for describing the internal organization of digital computers
    Can also be used to facilitate the design process of digital systems.
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 5
Register Transfer and Micro-operations 5 Lecture 6
Register Transfer Language
Registers are designated by capital letters, sometimes followed by numbers (e.g., A, R13, IR)
Often the names indicate function:
  MAR - memory address register
  PC - program counter
  IR - instruction register
Registers and their contents can be viewed and represented in various ways
  A register can be viewed as a single entity:
  Registers may also be represented showing the bits of data they contain
MAR
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 6
Register Transfer and Micro-operations 6 Lecture 6
Register Transfer Language
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
- a register
- portion of a register
- a bit of a register
Common ways of drawing the block diagram of a register
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register

## Slide 7
Register Transfer and Micro-operations 7 Lecture 6
Register Transfer Language
Copying the contents of one register to another is a register transfer
A register transfer is indicated as
  R2  R1
  In this case the contents of register R1 are copied (loaded) into register R2
  A simultaneous transfer of all bits from the source R1 to the destination register R2, during one clock pulse
  Note that this is a non-destructive; i.e. the contents of R1 are not altered by copying (loading) them to R2

## Slide 8
Register Transfer and Micro-operations 8 Lecture 6
Register Transfer Language
A register transfer such as
  R3  R5
  Implies that the digital system has
  the data lines from the source register (R5) to the destination register (R3)
  Parallel load in the destination register (R3)
  Control lines to perform the action

## Slide 9
Register Transfer and Micro-operations 9 Lecture 6
Control Functions
Often actions need to only occur if a certain condition is true
This is similar to an “if” statement in a programming language
In digital systems, this is often done via a control signal, called a control function
  If the signal is 1, the action takes place
This is represented as:
  P: R2  R1
  Which means “if P = 1, then load the contents of register R1 into register R2”, i.e., if (P = 1) then (R2  R1)
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 10
Register Transfer and Micro-operations 10 Lecture 6
Hardware Implementation of Controlled Transfers
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Clock
Transfer occurs here
R2
R1
Control
Circuit
Load
P
n
Clock
Load
t
t+1
The same clock controls the circuits that generate the control function and the destination register
Registers are assumed to use positive-edge-triggered flip-flops
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 11
Register Transfer and Micro-operations 11 Lecture 6
Basic Symbols in Register Transfer
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Examples
CSE 211, Computer Organization and Architecture Gagandeep Singh, CSE/IT

## Slide 12
Register Transfer and Micro-operations 12 Lecture 7
Overview
Register Transfer Language
Register Transfer
Bus and Memory Transfers
Arithmetic Micro-operations
Logic Micro-operations
Shift Micro-operations
Arithmetic Logic Shift Unit

## Slide 13
Register Transfer and Micro-operations 13 L
Connecting Registers - Bus Transfer
In a digital system with many registers, it is impractical to have data and control lines to directly allow each register to be loaded with the contents of every possible other registers
To completely connect n registers  n(n-1) lines
  This is not a realistic approach to use in a large digital system
Instead, take a different approach
Have one centralized set of circuits for data transfer – the bus
Have control circuits to select which register is the source, and which is the destination

## Slide 14
Register Transfer and Micro-operations 14 Le
Connecting Registers - Bus Transfer
From a register to bus: BUS  R
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0
Register A
Register B
Register C
Register D
Bus lines

## Slide 15
Register Transfer and Micro-operations 15 Le
Connecting Registers - Bus Transfer
Three-State Bus Buffers
Bus line with three-state buffers
Reg. R0
Reg. R1
Reg. R2
Reg. R3
Bus lines
2 x 4
Decoder
Load
D
0
D
1
D
2
D
3
z
w
Select
E (enable)
Output Y=A if C=1
High-impedence if C=0
Normal input A
Control input C
Select
Enable
0
1
2
3
S0
S1
A0
B0
C0
D0
Bus line for bit 0
From a Bus to Register
Bus R

## Slide 16
Register Transfer and Micro-operations 16
Memory - RAM
Memory (RAM) can be thought as a sequential circuits containing some number of registers
These registers hold the words of memory
Each of the registers is indicated by an address
These addresses range from 0 to r-1
Each register (word) can hold n bits of data
Assume the RAM contains r = 2k words. It needs the following
  n data input lines
  n data output lines
  k address lines
  A Read control line
  A Write control line
data input lines
data output lines
n
n
k
address lines
Read
Write
RAM
unit

## Slide 17
Register Transfer and Micro-operations 17 Lecture 7
Memory Transfer
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
AR
Memory
unit
Read
Write
Data in
Data out
M
Read : DR  M[AR]

## Slide 18
Register Transfer and Micro-operations 18 Lecture 7
Memory Read
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1
R1  M[MAR]

## Slide 19
Register Transfer and Micro-operations 19
Memory Write
To write a value from a register to a location in memory looks like this in register transfer language:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory
M[MAR]  R1

## Slide 20
Register Transfer and Micro-operations 20
A  B 1.Transfer content of reg. B into reg. A
AR DR(AD) 2.Transfer content of AD portion of reg. DR into reg. AR
A  constant 3.Transfer a binary constant into reg. A
ABUS  R1, R2 ← ABUS 4.Transfer content of R1 into bus A and, at the same time,
transfer content of bus A into R2
AR 5.Address register
DR 6.Data register
M[R] 7.Memory word specified by reg. R
M 8.Equivalent to M[AR]
DR  M 9.Memory read operation: transfers content of
memory word specified by AR into DR
M  DR 10.Memory write operation: transfers content of
DR into memory word specified by AR
SUMMARY OF R. TRANSFER MICROOPERATIONS

## Slide 21
Register Transfer and Micro-operations 21
Computer system microoperations are of four types:
Register transfer microoperations
Arithmetic microoperations
Logic microoperations
Shift microoperations
MICROOPERATIONS

## Slide 22
Register Transfer and Micro-operations 22
Arithmetic MICROOPERATIONS
Summary of Typical Arithmetic Micro-Operations
  R3  R1 + R2 Contents of R1 plus R2 transferred to R3
  R3  R1 - R2 Contents of R1 minus R2 transferred to R3
  R2  R2’ Complement the contents of R2
  R2  R2’+ 1 2's complement the contents of R2 (negate)
  R3  R1 + R2’+ 1 subtraction
  R1  R1 + 1 Increment
  R1  R1 - 1 Decrement
The basic arithmetic microoperations are
  Addition
  Subtraction
  Increment
  Decrement
The additional arithmetic microoperations are
  Add with carry
  Subtract with borrow
  Transfer/Load
  etc. …

## Slide 23
Register Transfer and Micro-operations 23
Overview
Register Transfer Language
Register Transfer
Bus and Memory Transfers
Arithmetic Micro-operations
Logic Micro-operations
Shift Micro-operations
Arithmetic Logic Shift Unit
CSE 211, Computer Organization and Architecture Gagandeep Singh CSE/IT

## Slide 24
Register Transfer and Micro-operations 24
Binary Adder
Binary Adder
CSE 211, Computer Organization and Architecture Gagandeep Singh CSE/IT

## Slide 25
Register Transfer and Micro-operations 25
Binary Adder-Subtractor
Binary Adder-Subtractor
CSE 211, Computer Organization and Architecture Gagandeep Singh CSE/IT

## Slide 26
Register Transfer and Micro-operations 26
Binary Incrementer
Binary Incrementer
CSE 211, Computer Organization and Architecture Gagandeep Singh CSE/IT

## Slide 28
Register Transfer and Micro-operations 28
CSE 211, Computer Organization and Architecture Gagandeep Singh CSE/IT
S1
S0
0
1
2
3
4x1
MUX
X0
Y0
C0
C1
D0
FA
S1
S0
0
1
2
3
4x1
MUX
X1
Y1
C1
C2
D1
FA
S1
S0
0
1
2
3
4x1
MUX
X2
Y2
C2
C3
D2
FA
S1
S0
0
1
2
3
4x1
MUX
X3
Y3
C3
C4
D3
FA
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0
1
S0
S1
Arithmetic Circuits

## Slide 29
Register Transfer and Micro-operations 29
Hardware Implementation
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 30
Register Transfer and Micro-operations 30
Applications of Logic Microoperations
Logic microoperations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
  Selective-set A  A + B
  Selective-complement A  A  B
  Selective-clear A  A • B’
  Mask (Delete) A  A • B
  Clear A  A  B
  Insert A  (A • B) + C
  Compare A  A  B

## Slide 31
Register Transfer and Micro-operations 31
Applications of Logic Microoperations
1. In a selective set operation, the bit pattern in B is used to set certain bits in A
1 1 0 0 At
1 0 1 0 B
1 1 1 0 At+1 (A  A + B)
If a bit in B is set to 1, that same position in A gets set to 1, otherwise that bit in A keeps its previous value
2. In a selective complement operation, the bit pattern in B is used to complement certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)
If a bit in B is set to 1, that same position in A gets complemented from its original value, otherwise it is unchanged

## Slide 32
Register Transfer and Micro-operations 32
Applications of Logic Microoperations
3. In a selective clear operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 0 0 At+1 (A  A  B’)
If a bit in B is set to 1, that same position in A gets set to 0, otherwise it is unchanged
4. In a mask operation, the bit pattern in B is used to clear certain bits in A 1 1 0 0 At
1 0 1 0 B
1 0 0 0 At+1 (A  A  B)
If a bit in B is set to 0, that same position in A gets set to 0, otherwise it is unchanged

## Slide 33
Register Transfer and Micro-operations 33
Applications of Logic Microoperations
5. In a clear operation, if the bits in the same position in A and B are the same, they are cleared in A, otherwise they are set in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)

## Slide 34
Register Transfer and Micro-operations 34
Applications of Logic Microoperations
6. An insert operation is used to introduce a specific bit pattern into A register, leaving the other bit positions unchanged
This is done as
  A mask operation to clear the desired bit positions, followed by
  An OR operation to introduce the new bits into the desired positions
  Example
    Suppose you wanted to introduce 1010 into the low order four bits of A:
    1101 1000 1011 0001 A (Original) 1101 1000 1011 1010 A (Desired)
    1101 1000 1011 0001 A (Original)
    1111 1111 1111 0000 Mask
    1101 1000 1011 0000 A (Intermediate)
    0000 0000 0000 1010 Added bits
    1101 1000 1011 1010 A (Desired)

## Slide 35
Register Transfer and Micro-operations 35
Shift Microoperations
There are three types of shifts
  Logical shift
  Circular shift
  Arithmetic shift
What differentiates them is the information that goes into the serial input
Serial
input
A right shift operation
A left shift operation
Serial
input

## Slide 36
Register Transfer and Micro-operations 36
Logical Shift
In a logical shift the serial input to the shift is a 0.
A right logical shift operation:
A left logical shift operation:
In a Register Transfer Language, the following notation is used
  shl for a logical shift left
  shr for a logical shift right
  Examples:
    R2  shr R2
    R3  shl R3
0
0

## Slide 37
Register Transfer and Micro-operations 37
Circular Shift
In a circular shift the serial input is the bit that is shifted out of the other end of the register.
A right circular shift operation:
A left circular shift operation:
In a RTL, the following notation is used
  cil for a circular shift left
  cir for a circular shift right
  Examples:
    R2  cir R2
    R3  cil R3

## Slide 38
Register Transfer and Micro-operations 38
Arithmetic Shift
An arithmetic shift is meant for signed binary numbers (integer)
An arithmetic left shift multiplies a signed number by two
An arithmetic right shift divides a signed number by two
The main distinction of an arithmetic shift is that it must keep the sign of the number the same as it performs the multiplication or division
A right arithmetic shift operation:
A left arithmetic shift operation:
0
sign
bit
sign
bit

## Slide 39
Register Transfer and Micro-operations 39
Arithmetic Shift
An left arithmetic shift operation must be checked for the overflow
0
V
Before the shift, if the leftmost two
bits differ, the shift will result in an
overflow
In a RTL, the following notation is used
  ashl for an arithmetic shift left
  ashr for an arithmetic shift right
  Examples:
    R2  ashr R2
    R3  ashl R3
sign
bit

## Slide 40
Register Transfer and Micro-operations 40
Hardware Implementation of Shift Microoperation
S
0
1
H0
MUX
S
0
1
H1
MUX
S
0
1
H2
MUX
S
0
1
H3
MUX
Select
0 for shift right (down)
1 for shift left (up)
Serial
input (IR)
A0
A1
A2
A3
Serial
input (IL)

## Slide 41
Register Transfer and Micro-operations 41
Arithmetic Logic and Shift Unit
Arithmetic
Circuit
Logic
Circuit
C
C
4 x 1
MUX
Select
0
1
2
3
F
S3
S2
S1
S0
B
A
i
A
D
A
E
shr
shl
i+1
i
i
i
i+1
i-1
i
i
  S3 S2 S1 S0 Cin Operation
  0 0 0 0 0 F = A
  0 0 0 0 1 F = A + 1
  0 0 0 1 0 F = A + B
  0 0 0 1 1 F = A + B + 1
  0 0 1 0 0 F = A + B’
  0 0 1 0 1 F = A + B’+ 1
  0 0 1 1 0 F = A - 1
  0 0 1 1 1 F = A
  0 1 0 0 X F = A  B
  0 1 0 1 X F = A B
  0 1 1 0 X F = A  B
  0 1 1 1 X F = A’
  1 0 X X X F = shr A
  1 1 X X X F = shl A