## Slide 1: Computer Organization and design

## Slide 2: INTRODUCTION
Every different processor has its own design
(different registers, buses, micro-operations, machine instructions, etc)
Modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
  Etc.
However, to understand how processors work, use a simplified processor model
This is similar to what real processors were like ~25 years ago

## Slide 3: THE BASIC COMPUTER
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 4: INSTRUCTIONS
Instruction codes
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operation)
The instructions of a program, along with any needed data are stored in memory
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control circuitry in control unit then translates the instruction into the sequence of microoperations necessary to implement it

## Slide 5: INSTRUCTION FORMAT
Instruction codes
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 6: ADDRESSING MODES
Instruction codes
The address field of an instruction can represent either
  Direct address: the address in memory of the data to use (the address of the operand), or
  Indirect address: the address in memory of the address in memory of the data to use
Effective Address (EA)
  The address, that can be directly used without modification to access an operand for a computation-type instruction, or as the target address for a branch-type instruction
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 7: PROCESSOR REGISTERS
Instruction codes
A processor has many registers to hold instructions, addresses, data, etc
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction
  Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing: The Address Register (AR) is used for this
  The AR is a 12 bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR). The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 8: PROCESSOR REGISTERS
Instruction codes
The significance of a general purpose register is that it can be used for loading operands and storing results
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data; in the Basic Computer this is the Temporary Register (TR)
The Basic Computer uses a very simple model of input/output (I/O) operations
  Input devices are considered to send 8 bits of character data to the processor
  The processor can send 8 bits of character data to output devices
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 9: BASIC COMPUTER REGISTERS
List of Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 10: COMMON BUS SYSTEM
Registers
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 11: COMMON BUS SYSTEM
Registers
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6

## Slide 12: COMMON BUS SYSTEM
Registers
AR
PC
DR
L
I
C
L
I
C
L
I
C
AC
L
I
C
ALU
E
IR
L
TR
L
I
C
OUTR
L
INPR
Memory
4096 x 16
Address
Read
Write
16-bit Common Bus
7
1
2
3
4
5
6
S0
S1
S2

## Slide 13: COMMON BUS SYSTEM
Registers
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register

## Slide 14: BASIC COMPUTER INSTRUCTIONS
Instructions
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 15: BASIC COMPUTER INSTRUCTIONS
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off
Instructions

## Slide 16: INSTRUCTION SET COMPLETENESS
Instruction Types
Set of instructions using which user can construct machine language programs to evaluate any computable function.
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  - ADD, CMA, INC, CIR, CIL, AND, CLA
  Transfer Instructions
  - Data transfers between the main memory
  and the processor registers
  - LDA, STA
  Control Instructions
  - Program sequencing and control
  - BUN, BSA, ISZ
  Input/Output Instructions
  - Input and output
  - INP, OUT
Instructions

## Slide 17: TIMING AND CONTROL
Control unit of Basic Computer
Timing and control
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 18: TIMING SIGNALS
- Generated by 4-bit sequence counter and 416 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC  0
Timing and control

## Slide 19: INSTRUCTION CYCLE
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction and calculate effective address (EA)
  Read the EA from memory if the instruction has an indirect address
  (Fetch operand)
  4. Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction

## Slide 20: FETCH and DECODE
• Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0
Instruction Cycle

## Slide 21: DETERMINE THE TYPE OF INSTRUCTION
= 0 (direct)
D'7IT3: AR M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.
Instrction Cycle
Start
SC  0
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference) =>opcode ≠ 111
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 22: REGISTER REFERENCE INSTRUCTIONS
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Instruction Cycle
Register Reference Instructions are identified when

## Slide 23: MEMORY REFERENCE INSTRUCTIONS
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to complete in a CPU cycle
- The execution of MR instruction starts with T4
MR Instructions
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, AR  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 24: MEMORY REFERENCE INSTRUCTIONS
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
Memory
Memory
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address

## Slide 25: MEMORY REFERENCE INSTRUCTIONS
MR Instructions
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 26: FLOWCHART FOR MEMORY REFERENCE INSTRUCTIONS
MR Instructions
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 27: INPUT-OUTPUT AND INTERRUPT
Input-Output Configuration
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit
- The terminal sends and receives serial information
- The serial info. from the keyboard is shifted into INPR
- The serial info. for the printer is stored in the OUTR
- INPR and OUTR communicate with the terminal
serially and with the AC in parallel.
- The flags are needed to synchronize the timing
difference between I/O device and the computer
A Terminal with a keyboard and a Printer
I/O and Interrupt
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 28: PROGRAM CONTROLLED DATA TRANSFER
/* Input */ /* Initially FGI = 0 */
loop: If FGI = 1 goto loop
INPR  new data, FGI  1
loop: If FGO = 1 goto loop
consume OUTR, FGO  1
-- CPU -- -- I/O Device --
loop: If FGI = 0 goto loop
AC  INPR, FGI  0
/* Output */ /* Initially FGO = 1 */
loop: If FGO = 0 goto loop
OUTR  AC, FGO  0
I/O and Interrupt
Start Input
FGI=0
AC  INPR
More
Character
END
Start Output
FGO  1
FGO=1
More
Character
END
consume OUTR
yes
no
yes
no
FGI=0
FGO=1
yes
yes
no
no

## Slide 29: INPUT-OUTPUT INSTRUCTIONS
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off
CPU Side

## Slide 30: PROGRAM-CONTROLLED INPUT/OUTPUT
Program-controlled I/O
- Continuous CPU involvement
I/O takes valuable CPU time
- CPU slowed down to I/O speed
- Simple
- Least hardware
I/O and Interrupt
Input
LOOP SKI DEV
BUN LOOP
INP DEV
Output
LDA DATA
LOOP SKO DEV
BUN LOOP
OUT DEV

## Slide 31: INTERRUPT INITIATED INPUT/OUTPUT
- Open communication only when some data has to be passed --> interrupt.
- The I/O interface, instead of the CPU, monitors the I/O device.
- When the interface founds that the I/O device is ready for data transfer,
it generates an interrupt request to the CPU
- Upon detecting an interrupt, the CPU stops momentarily the task
it is doing, branches to the service routine to process the data
transfer, and then returns to the task it was performing.
* IEN (Interrupt-enable flip-flop)
- can be set and cleared by instructions
- when cleared, the computer cannot be interrupted

## Slide 32: FLOWCHART FOR INTERRUPT CYCLE
R = Interrupt f/f
- The interrupt cycle is a HW implementation of a branch
and save return address operation.
- At the beginning of the next instruction cycle, the
instruction that is read from memory is in address 1.
- At memory address 1, the programmer must store a branch instruction
that sends the control to an interrupt service routine
- The instruction that returns the control to the original
program is "indirect BUN 0"
I/O and Interrupt
Store return address
R
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
IEN
FGI
FGO
Execute
instructions
R  1
=1
=1
=1
=0
=0
=0

## Slide 33: REGISTER TRANSFER OPERATIONS IN INTERRUPT CYCLE
Register Transfer Statements for Interrupt Cycle
- R F/F  1 if IEN (FGI + FGO)T0T1T2
 T0T1T2 (IEN)(FGI + FGO): R  1
- The fetch and decode phases of the instruction cycle
must be modified Replace T0, T1, T2 with R'T0, R'T1, R'T2
- The interrupt cycle :
RT0: AR  0, TR  PC
RT1: M[AR]  TR, PC  0
RT2: PC  PC + 1, IEN  0, R  0, SC  0
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256
I/O and Interrupt

## Slide 34: COMPLETE COMPUTER DESCRIPTION Flowchart of Operations
Description
=1 (I/O) =0 (Register) =1(Indir) =0(Dir)
start
SC  0
R
AR  PC
R’T0
IR  M[AR], PC  PC + 1
R’T1
AR  IR(0~11), I  IR(15)
D0...D7  Decode IR(12 ~ 14)
R’T2
AR  0, TR  PC
RT0
M[AR]  TR, PC  0
RT1
PC  PC + 1, IEN  0
R  0, SC  0
RT2
D7
I
I
Execute
I/O
Instruction
Execute
RR
Instruction
AR <- M[AR]
Idle
D7IT3 D7I’T3
D7’IT3 D7’I’T3
Execute MR
Instruction
=0(Instruction =1 (interrupt
Cycle) Cycle)
=1(Register or I/O) =0(Memory Ref)
D7’T4
IEN
FGI
FGO
=1
=1
=1
=0
=0
=0
R  1

## Slide 35: COMPLETE COMPUTER DESCRIPTION Microoperations
Description
Fetch
Decode
Indirect
Interrupt
Memory-Reference
AND
ADD
LDA
STA
BUN
BSA
ISZ
RT0:
RT1:
RT2:
D7IT3:
RT0:
RT1:
RT2:
D0T4:
D0T5:
D1T4:
D1T5:
D2T4:
D2T5:
D3T4:
D4T4:
D5T4:
D5T5:
D6T4:
D6T5:
D6T6:
AR  PC
IR  M[AR], PC  PC + 1
D0, ..., D7  Decode IR(12 ~ 14),
AR  IR(0 ~ 11), I  IR(15)
AR  M[AR]
R  1
AR  0, TR  PC
M[AR]  TR, PC  0
PC  PC + 1, IEN  0, R  0, SC  0
DR  M[AR]
AC  AC  DR, SC  0
DR  M[AR]
AC  AC + DR, E  Cout, SC  0
DR  M[AR]
AC  DR, SC  0
M[AR]  AC, SC  0
PC  AR, SC  0
M[AR]  PC, AR  AR + 1
PC  AR, SC  0
DR  M[AR]
DR  DR + 1
M[AR]  DR, if(DR=0) then (PC  PC + 1),
SC  0
T0T1T2(IEN)(FGI + FGO):

## Slide 36: COMPLETE COMPUTER DESCRIPTION Microoperations
Register-Reference
CLA
CLE
CMA
CME
CIR
CIL
INC
SPA
SNA
SZA
SZE
HLT
Input-Output
INP
OUT
SKI
SKO
ION
IOF
D7IT3 = r
IR(i) = Bi
r:
rB11:
rB10:
rB9:
rB8:
rB7:
rB6:
rB5:
rB4:
rB3:
rB2:
rB1:
rB0:
D7IT3 = p
IR(i) = Bi
p:
pB11:
pB10:
pB9:
pB8:
pB7:
pB6:
(Common to all register-reference instr)
(i = 0,1,2, ..., 11)
SC  0
AC  0
E  0
AC  AC
E  E
AC  shr AC, AC(15)  E, E  AC(0)
AC  shl AC, AC(0)  E, E  AC(15)
AC  AC + 1
If(AC(15) =0) then (PC  PC + 1)
If(AC(15) =1) then (PC  PC + 1)
If(AC = 0) then (PC  PC + 1)
If(E=0) then (PC  PC + 1)
S  0
(Common to all input-output instructions)
(i = 6,7,8,9,10,11)
SC  0
AC(0-7)  INPR, FGI  0
OUTR  AC(0-7), FGO  0
If(FGI=1) then (PC  PC + 1)
If(FGO=1) then (PC  PC + 1)
IEN  1
IEN  0
Description

## Slide 37: DESIGN OF BASIC COMPUTER(BC)
Hardware Components of BC
A memory unit: 4096 x 16.
Registers:
AR, PC, DR, AC, IR, TR, OUTR, INPR, and SC
Flip-Flops(Status):
I, S, E, R, IEN, FGI, and FGO
Decoders: a 3x8 Opcode decoder
a 4x16 timing decoder
Common bus: 16 bits
Control logic gates:
Adder and Logic circuit: Connected to AC
Control Logic Gates
  - Input Controls of the nine registers
  - Read and Write Controls of memory
  - Set, Clear, or Complement Controls of the flip-flops
  - S2, S1, S0 Controls to select a register for the bus
  - AC, and Adder and Logic circuit
Design of Basic Computer